## Slide 1: Worked Example
PLP with Levinson–Durbin

## Slide 2: speech signal
Consider the following short speech sequence: x[n]=[1,2,3,4,2,1,0,-1]
Assume:
Sampling frequency Fs=8000Hz
Frame length = 4 samples
No overlap
LPC/PLP order = 2
We will process the first frame.

## Slide 3
Step 1: Framing
The speech signal is divided into frames of 4 samples.
Frame1: x1​[n]=[1,2,3,4]
Frame2; x2​[n]=[2,1,0,−1]
For this problem use x1​[n]=[1,2,3,4]
Step 2: Windowing
To keep the numerical example manageable, we assume a rectangular window:
w[n]=1
xw​[n]=x[n]w[n]
therefore
xw​[n] =[1,2,3,4]
In a real PLP system, a Hamming window is normally used.

## Slide 4: Step 3: Autocorrelation
R(k)=
Since we need a second-order model, calculate:
R(0),R(1),R(2)
Calculate R(0)
R(0)=12+22+32+42
=1+4+9+16 = 30
Calculate R(1)
R(1)= (1)(2)+(2)(3)+(3)(4) =2+6+12 $$
R(1)= 20
Calculate R(2)
R(2)= (1)(3)+(2)(4) =3+8
R(2)=11
​
​

## Slide 5: Step 4: Levinson–Durbin Algorithm
E0​=R(0)=30
Iteration 1 : The first reflection coefficient is:
K1= = ​ =0.6667
=0.6667
​
E1​=(1−​)E0​
=(30)
=(1−0.4444)(30)
E1​≈16.6667​

## Slide 6: Step 5: Second Levinson–Durbin iteration
Calculate :
K2​=​
K2​=
Update ​
The Levinson–Durbin update is:
=0.6667−(−0.14)(0.6667)
=0.6667+0.0933
α1​=0.7600
α2​=K2​=−0.14
Final prediction error
=(1−0.142)(16.6667)
E2​≈16.34
The LPC polynomial is: A(z)=1−a1​z−1−a2​z−2 =1−0.76z−1+0.14z−2
and the vocal-tract model is:

## Slide 7: Step 6: Obtain the LPC spectrum
For PLP, we need the spectral representation.
The LPC power spectrum is:
=1−0.76z−1+0.14z−2
To keep the arithmetic simple, use four frequency points
ω=0,π/2​,π,3π/2​
Frequency point 1: ω=0
e−j0=1, e−j2(0)=1
A(0)=1−0.76+0.14 =0.38
P(0) =

## Slide 8
Frequency point 2: ω=
e−j=-1, e−jπ=-1
A()=1−0.76(-j)+0.14(-1) =0.86+j0.76
∣A(π/2)∣2=0.862+0.762 =1.3172
P() =
Frequency point 3: ω=π
e−jπ=−1 e−j2π=1
A(π)=1−0.76(−1)+0.14(1)
=1+0.76+0.14 = 1.90
P() =

## Slide 9: Step 7: Convert frequencies to Bark scale
The Bark conversion can be approximated by:
B(f)=13tan−1(0.00076f)+3.5tan−1
Since Fs= 8000Hz
the corresponding frequencies are approximately: 0,2000,4000 Hz
B(2000) ≈13.1 Bark
B(4000)≈19.0 Bark
Thus the spectrum is represented on a perceptually motivated frequency scale.​

## Slide 10: Step 8: Bark auditory filtering
In an actual PLP implementation, the LPC spectrum is passed through a critical-band filterbank.
To demonstrate the auditory weighting, suppose the simplified Bark-filter responses are:
WB =[0.80,1.00,0.70]
PB​=P×WB​
PB​(1)=113.16(0.8)=90.53
PB​(2)=12.41(1)=12.41
PB​(3)=4.53(0.7)=3.17

## Slide 11
Step 9: Equal-loudness weighting
let the equal-loudness weights be:
WE​=[0.50,1.00,1.20]
PE​=PB​×WE​
Low frequency: 90.53(0.50) =45.27
Middle frequency: 12.41(1) =12.41
High frequency : 3.17(1.20) =3.80
Step 10: Loudness compression
PLP applies a cube-root compression:
PC​=
45.271/3≈3.56
12.411/3≈2.32
3.801/3≈1.56
PC​=[3.56,2.32,1.56]​
This is the perceptually modified spectrum.

## Slide 12: Step 11: Convert perceptual spectrum back to autocorrelation
This is where PLP comes back to an LPC-like representation.
We need a symmetric spectrum. Let us use:
PC=[3.56,2.32,1.56,2.32]
The last value mirrors the second value.
Calculate Rp(0)
Rp​(0)=1/4​(3.56+2.32+1.56+2.32)=2.44
Rp​(1)=0.50​
Rp​(2)=0.12

## Slide 13: Step 12: All-pole approximation using Levinson–Durbin
Now we fit an all-pole model to the perceptually modified spectrum.
First iteration: K1​=
Prediction error: E1
Second iteration : k20.0075
α1​≈0.2034​ α2 ≈0.0075
Therefore the final PLP all-pole model is approximately:

## Slide 14: Two Levinson–Durbin operations
Stage | Input | Output
First LD | Speech autocorrelation | LPC coefficients
PLP processing | LPC spectrum → Bark → equal-loudness → compression | Perceptual spectrum
Second LD / all-pole fitting | Perceptual-spectrum autocorrelation | PLP all-pole coefficients